High-performance door ASSA ABLOY RP400 Machine Protection

Description:

Flexible High-performance door, opening in vertical direction for use as a machine protection door.

Self-supporting side frames made of aluminium with integreated safety switches, all fittings galvanized. Front of side frame lifts of for generous access to safety limit switches and fixtures.

Door curtain made of RollTex® Plus (TRAV-Certificate) – colour

- Blue 	(similar RAL 5002)

- Orange	(similar RAL 2009)

- Grey 	(similar RAL 7001).

Wind protection: through wind tabs on the door curtain

Wind resistance: class 1 (EN 12424) up to max. 11 m²

Bottom profile: anodized aluminium.

Drive unit: hollow shaft gear motor, rotable in steps of 45°

Protection: IP 55

Control system: Frequency converter control system MCC, based on Vector control and including boost function at start-up. Can be upgraded with a graphic display and foil keypad for easy guided operation. Easy access to all important information for operation and service.

Control voltage: 24 V DC

Supply voltage:

MCC: 3/(N)/PE/380/400/415/440/460/480V (+/- 10%); 50/60 Hz.

Other voltages on request.
UL-Version: 3L/(N)PE/208/220/230/460/480V;60Hz

Safety devices:

- Electrical safety contact edge

- Door line photocell

- Drop down protection integrated in gear box

- Flush bottom profile

- Safety switches: Magnetic switch with evaluation unit for performance level e, acc. to EN ISO 13849-1, and SIL3, acc. to EN 62061, integrated in side frame.

Manual activation: by means of a crank.

Opening / closing speed: max 2.4/1.3 m/s (depending on size)

Size max.:

ASSA ABLOY RP400

(DW min./max.) 750mm / 4000 mm

(DH min./max.)  750mm / 3500 mm

Brand: ASSA ABLOY RP400 Machine Protection Door

Option

Cover

- Top roll cover:made of anodized aluminum

- Motor cover: made of anodized aluminium

Door curtain (alternatively):

- RollTex Original TRAV Certificate in color:

- Blue 	(similar RAL 5002),

- Orange (similar RAL 2009)

- Grey 	(similar RAL 7001)

- NomaTex in color:

- Grey 	(similar RAL 7038)

- Blue 	(similar RAL 5005)

- Orange (similar RAL 2009)

- Yellow 	(similar 1023)

- Red 	(similar RAL 3000)

- Rolltex Plus and RollTex Original with window

- NomaTex with window or vision panels

- Window Anti-UV bronze coloured window, EN 1598 
(only for Curtain RollTex® and NomaTex®)

- Flame retardant door blade B1 
- Color Orange (similar RAL 2008)

- PVC with colored fabric reinforcemet strips:

- Grey	(similar RAL 7037)

- Blue 	(similar RAL 5002)

- Orange (similar RAL 2011)

- Yellow 	(similar RAL 1021)

- Red 	(similar RAL 3002)

- White 	(similar RAL 9010)

- Black 	(similar RAL 9005)

- PVC with colored fabric reinforcement strips silicone-free

Safety devices:

- Pre running photocell

- Light curtain

Safety switches (alternatively)

- 2 pcs Schmersal magnetic switches with control unit for safety class 4, Ple, SIL3, switches integrated in the side frames

- 2 pcs Telemecanique limit switches with control unit for safety class 3, PLd, SIL3, switches integrated in the side frames

- 1 pc Telemecanique limit switch on the drive side, no safety class

- 2 pcs Telemecanique limit switches, no safety class

Miscellaneous:

- Graphic display for MCC VectorControl unit

- Bottom plates in the side frames

- Door support for floor assembly

- Chain drive

- X-level extensions of the side frames from the lower closing edge to the floor

- Extended flexible seal

- Actuator

- Additional safety devices